100-Hour/Annual Inspection

Checklist (GA)

Part 23 & CAR 3 Aircraft

Original Issue date April 1998, Current revision date April 29, 2011

Reference Data:

Order 8130.2, CAR-3, CFR 21 Certification, CFR 23 Airworthiness Standards, CFR 43 Maintenance, CFR 45 Markings, CFR 47 Registered properly, CFR 91 Pilot Responsibility, CFR 36 Noise, CFR 33 engines, CFR 39 AD’s, CFR 145 Repair Stations and AC 43.13-1B & 2A Major Repair and Alterations, Manufacture Maintenance Manuals.

INTERPRETATION OF THE TERM “AIRWORTHY”

Section 44704(d) of 49 U.S.C

- The aircraft must conform to its type certificate.

- When aircraft configuration and the components installed are consistent with drawings, specifications, and other data that are part of the type certificate (T/C), and include any supplemental T/C and field approval alterations incorporated into the aircraft.

- The aircraft must be in condition for safe operation.

- Aircraft relative to wear and deterioration i.e., corrosion, fluid leaks, tire wear, window delimitation/crazing.

NOTE:  If one or both of these conditions are not met, the aircraft would be considered unairworthy.

NOTE:  This is only a guide and should not be considered FAA approved data for 100 hour or annual inspection checklist.  Consult CFR 43 subpart D, for scope and detail of items to be included for 100 hour or annual inspections.  This checklist is not exhaustive and does not supersede Manufacture’s publications and is up-dated periodically!

The owner or operator is responsible for the maintaining the aircraft in an airworthy condition, including compliance with all applicable Airworthiness Directives as specified in Part 39 of the Code of Federal Regulations and “Airworthiness Limitations” of the applicable manufactures manual.  It is also the responsibility of the owner to insure that the aircraft is inspected in compliance with the requirement of Part 21, 43, and 91 of Code of Federal Regulations.

Aircraft Data

- N-Number: N__________________________________

- Airframe Type Certificate No. _____________________ Rev. _______ Specification sheet ____________

- ASTM No._____________________________________ Rev. _______ N/A

- Aircraft Model _________________________________ Model No. ______________________________

- Aircraft Serial No. ______________________________ Year manufactured ________________________

- Certification Basis: CAR or FAR ___________________________________________________________

### Airman Attitude

- Has Constructive attitude toward Compliance		Order 2150.3A par. 205	Yes  No  N/A

- Verify A&P/IA certificate number and picture ID		CFR 65.91 		Yes  No  N/A

- Verify Pilots certificate number and picture ID			CFR 61.3 	Yes  No  N/A

# Data

- FAA-approved maintenance manuals available			CFR 43.13. 	Yes  No  N/A

- Alterations IAW approved STC/TSO/PMA/Field approval or other FAA data, (337’s) 										CFR 21.97/101/113 	Yes  No  N/A

- Instructions for Continued Airworthiness	CFR 21.31, 21.50, 23.1529	Yes  No  N/A

- Type Certificate Data Sheet (TCDS)			CFR 21.41/ CAR 3.15	Yes  No  N/A

- Aircraft Flight Manual / Pilot Operating Hand book	CFR 21.5/CAR 3.72	Yes  No  N/A

- AFM/POH Date ______________________ Rev. No. ____________________ 	Yes  No  N/A

- Data plate aircraft 						CFR 45.13	Yes  No  N/A

- Data plate aircraft MFG before March 7, 1988 Make/model & S/N CFR 45.11(d)	Yes  No  N/A

- Data plate engine on engine make and model/serial number CFR45.11 & 21.182	Yes  No  N/A

- Data plates critical components				CAR 3.18 CFR 45.15	Yes  No  N/A

- Data plates Life Limited Parts					CFR 45.16	Yes  No  N/A

Records

- Registration current and in aircraft (NO photo copy)	CFR 91.9 / CAR 3.792	Yes  No  N/A

- Airworthiness Certificate in aircraft dated and signed	CFR 91.203(a) & 21.175	Yes  No  N/A

- Annual Inspection Total time________ Description of work accomplished _____Date completed______ and A&P/IA Signature _______ 				CFR 43.11 & 91.417 	Yes  No  N/A

- All AD’s, recorded in maintenance records and check recurring AD’s

- Airframe						CFR 39 & 91.417	Yes  No  N/A

- Engine							CFR 39 & 91.417	Yes  No  N/A

- Propeller						CFR 39 & 91.417	Yes  No  N/A

- Appliances  	Check for a list of items			CFR 39 & 91.417	Yes  No  N/A

- Reduce Vertical Separation Minimums (RVSM) with Letter of Authorization (LOA) 											CFR 91.706	Yes  No  N/A

- Last Annual inspection completed: date __________________  	CFR 43.11 & 91.417

- CFR 65.91 IA Name ________________ Certification No.______________	Yes  No  N/A

- 145 Repair station sign off date Repair Station number _________________	Yes  No  N/A

- Last Progressive Inspection phase signed of date			CFR 91.409(d)	Yes  No  N/A

    - Phase inspection dated and signed by A&P/IA 		CFR 91.409(d)(1)Yes  No  N/A

    - 145 Repair station number ________________ 	CFR 145.5/107/201/204	Yes  No  N/A

- Last 100-hour inspection date ___________ Total time  ________	CFR 91.405(b)

- 145 Repair station number ________________ 	CFR 145.5/107/201/204	Yes  No  N/A

- A&P sign off date ______ Certification No, _______CFR 43.15, 65.85, 91.409 Yes  No  N/A

- A&P/IA Signature __________________________	CFR 43.11 & 91.417 	Yes  No  N/A

- Equipment list current and in aircraft 		CAR-3.73 and CFR 23.29 & 91.9	Yes  No  N/A

- Equipment list up-dated to match conformity of aircraft 	CAR 3.777 CFR 91.9	Yes  No  N/A

- Status of Life Limited parts Effective 04- 15-2002		CFR 43.10	Yes  No  N/A

- Current approved flight manual after 03-1-1979 in aircraft CFR 21.5/23.1581, 91.9	Yes  No  N/A

- Current flight manual POH before 03-1-1979 in aircraft Yes  No  Revision number/date ____________ Limitations and placards CAR 3.778 CFR 21.5, 21.1559, 23.1581, 91.9		Yes  No  N/A

- Current weight & balance report dated & signed CAR 3.71, 23.1519, 23.1581, 91.9	Yes  No  N/A

- Identification data plate secured to aircraft fuselage exterior 	CFR 45.11	Yes  No  N/A

- If applicable, check the MEL to determine that:			CFR 91.213	Yes  No  N/A

- Issued by N-number and serial number to the aircraft operator 			Yes  No  N/A

- A Letter of Authorization (LOA) from a district office; check deferred items for placards and dates											Yes  No  N/A

- Maintenance Records for each Engine, Propeller, Airframe and Appliances inaccordance with 											CFR 91.417 	Yes  No  N/A

- ATC transponder date ___ 24 calendar months check. 	CFR 91.413 & 23.1301	Yes  No  N/A

- ELT TSO-C91a /TS0-C126 every 12 months check date 06/21/1985CFR 91.207	Yes  No  N/A

- Altimeter test every 24 months.	CFR 91.411and CFR 43 Appendix E	Yes  No  N/A

- Pitot static transponder test every 24 months	CAR 3.665CFR 43 Appendix F	Yes  No  N/A

- Deferred items under Part 91.213 for Day VFR			CFR 91.213	Yes  No  N/A

- Is the item placarded							Yes  No  N/A

- Is there a maintenance record entry						Yes  No  N/A

- Is the item disabled or removed						Yes  No  N/A

### Cockpit Inspection

- Placards read correctly Instrument & placards are correctly located per POH/AFM & TCDS 	CFR 23.1541-1567/ CAR 3.755						CFR 91.31	Yes  No  N/A

- INOP placards 						CFR 91.213	Yes  No  N/A

- INOP instruments disabled or removed by an A&P		CFR 91.213	Yes  No  N/A

- Equipment list up-dated					CFR 91.213	Yes  No  N/A

- Maintenance record entry					CFR 91.213	Yes  No  N/A

- Weight and balance record updated				CFR 91.9	Yes  No  N/A

- Minimum Equipment List (MEL) for aircraft			CFR 91.213(a)(1)Yes  No  N/A

- Vacuum indicating system, Life limited pump			CFR 23.1301	Yes  No  N/A

- Compass card Yes  No  Readable 	CAR 3,385 CFR 23.1547 & 25.1547	Yes  No  N/A

- Additional instruments not on equipment list or Form 337 CAR 3.661CFR 21.113	Yes  No  N/A

- Type of clock installed original analog or digital working 		AC 20-94	Yes  No  N/A

- Nav Radio P/N 1 _________, P/N 2 ________ matches equipment list		Yes  No  N/A

- Conforms to Type Certificate (TC) per POH/AFM see item (5,6)			Yes  No  N/A

- Cockpit fuel smell 					CAR 3.440 / CFR 23.863	Yes  No  N/A

- Data plate information matches registration 		CFR 45.11/13 & 47.3	Yes  No  N/A

- Intercom jack, how many any extra ____and required Form 337 			Yes  No  N/A

- Fire extinguisher gage      Green  Red  			CFR 23.1199	Yes  No  N/A

- Fire Extinguishing Agent commuter category installed		CFR 23.1197	Yes  No  N/A

- Fire extinguisher easy access to pilot				CFR 23.851	Yes  No  N/A

- Oxygen equipment and supply lines condition 		CFR 23.1441thru1453	Yes  No  N/A

- Oxygen bottle if required Green  Red  			CFR 23.1441	Yes  No  N/A

Hydro AA 5 years HT 3 year retire at 24 years 		AC 43.13-1b para 9-51	Yes  No  N/A

- Instrument filter covers installed 						Yes  No  N/A

- Yoke chain safety wired, loose or corrosion present		CFR 43.13	Yes  No  N/A

- Cockpit control knob shape correct type			CAR 3.384 CFR 23.781	Yes  No  N/A

- Flap, gear, knobs installed 				CAR 3.384 CFR 23.781	Yes  No  N/A

- Electrical wiring more than ½ inch slack 		AC 43.13-1B para 11-118	Yes  No  N/A

- Electrical wiring clamps/marking as required 		AC 43.13-1B sec. 11	Yes  No  N/A

- Tie-wraps items of mass in the cabin 				CFR 23.561	Yes  No  N/A

- Loose wires under dash not clamped 				CFR 23.1351	Yes  No  N/A

- Fuel selector moves to all positions and placarded 	CAR 3.364 CFR 23.951	Yes  No  N/A

- Brake master cylinder leaking R/H  L/H  			CRF 43.13	Yes  No  N/A

- Thoroughly clean the aircraft and aircraft engine 			CFR 43App D	Yes  No  N/A

- Cargo tie downs or nets if installed				CFR 91.525	Yes  No  N/A

- General, uncleanness and loose equipment that might foul the controls, apparent and obvious defects and insecurity of attachment.					CRF 43App D	Yes  No  N/A

- Stall warning system horn works			CAR 3.120 CFR 23.1323	Yes  No  N/A

- Windshield STC for one piece				CFR 43 Appendix A	Yes  No  N/A

- Windows tinted					TCDS/Equipment list	Yes  No  N/A

- Sun visor installation or STC with form 337			CFR 43.13	Yes  No  N/A

- Windshield and windows conditions			CAR 3.382 CFR 23.775	Yes  No  N/A

- Windscreen clear  scratches  cracks  crazing  											Reference CFR23.775 AC 43.13-1b and MIL-P-5425	Yes  No  N/A

- Windows stopped drilled, cracked, or crazed 						CAR 3.382 CFR 23.775, and AC 43.13-1B Chapter 3 paragraph 318 (a)(2), and MIL-P-5425 	Yes  No  N/A

# Instruments							CFR 91.205

## Flight Instruments minimum required

- An Airspeed indicator					CAR 3.655CFR 23.1303	Yes  No  N/A

- An Altimeter indicator				CAR 3.655 CFR 23.1303	Yes  No  N/A

- Direction indicator					CAR-3.666 CFR 23.1303	Yes  No  N/A

Minimum Instruments Required Visual-flight rules (day)

- Air speed indicator					CAR 3.655 CFR 91.205(b)Yes  No  N/A

- Altimeter						CAR 3.655 CFR 91.205(b)Yes  No  N/A

- Magnetic direction indicator				CAR 3.655 CFR 91.205(b)Yes  No  N/A

- Tachometer for each engine				CAR 3.655 CFR 91.205(b)Yes  No  N/A

- Oil pressure gauge for each engine using pressure system	CAR 3.655 CFR 91.205(b)Yes  No  N/A

- Manifold pressure gauge for each altitude engine		CAR 3.672 CFR 91.205(b)Yes  No  N/A

- Fuel gauge indicating the quantity of fuel in each tank		CFR 91.205(b)	Yes  No  N/A

- Landing gear position indicator, if retractable 			CFR 91.205(b)	Yes  No  N/A

Minimum Instrument for Instrument flight rules

- Two-way radio communications and navigation equipment	CFR 91.205(c)	Yes  No  N/A

- Gyroscopic rate-of-turn indicator			CAR 3.668 CFR 91.205(c)Yes  No  N/A

- Slip-skid indicator						CFR 91.205(c)	Yes  No  N/A

- Sensitive altimeter adjustable for barometric pressure		CFR 91.205(c)	Yes  No  N/A

- Clock displaying hours, minutes, and seconds with sweeping second hand pointer or digital presentation									CFR 91.205(c)	Yes  No  N/A

- Generator or alternator of adequate capacity			CFR 91.205(c)	Yes  No  N/A

- Gyroscopic pitch and bank indicator (artificial horizon)		CFR 91.205(c)	Yes  No  N/A

- Gyroscopic direction indicator (directional gyro)			CFR 91.205(c)	Yes  No  N/A

Powerplant Instrument (all aircraft) CAR –3 Subpart F and Part 23

- Fuel quantity indicator per tank			CAR 3.672 CFR 23.1305(a)	Yes  No  N/A

- Oil pressure indicator for each engine		CAR 3.674 CFR 23.1305(a)	Yes  No  N/A

- Oil temperature indicator for each engine			CFR 23.1305(a)	Yes  No  N/A

- Oil quantity measuring device for each engine	CAR 3.674 CFR 23.1305(a)	Yes  No  N/A

- Fire warning indicator if required by				CFR 23.1205	Yes  No  N/A

- Tachometer indicator for each engine				CFR 23.1305(b)	Yes  No  N/A

- Cylinder head indicator for each engine				CFR 23.1305(b)	Yes  No  N/A

a.  Cowl flaps installed			CAR 3.675 CFR 23.1305(b)	Yes  No  N/A

b.  Commuter category aircraft					CFR 23.1305(b)	Yes  No  N/A

- Manifold pressure indicator for each engine and for each engine with an controllable pitch propeller										CFR 23.1305(b)	Yes  No  N/A

Instrument Arrangement			CAR 3.661 	CFR 23.1321

- Attitude indicator on panel top center position			CFR 23.1321	Yes  No  N/A

- Airspeed indicator adjacent to and directly to left of the instrument in the top center position.											CFR 23.1321	Yes  No  N/A

- Altitude indicator adjacent to and directly to right of the instrument in the top center position.											CFR 23.1321	Yes  No  N/A

- Magnetic direction indicator placard must state whether the calibration was made with radio receivers on or off									CFR 23.1547	Yes  No  N/A

- Magnetic direction indicator more than 10 degrees off		CFR 23.1547	Yes  No  N/A

Instrument Markings			CAR 3.755	CFR 23.1543

- Marking on cover glass must be in alignment with face		CFR 23.1543	Yes  No  N/A

- Each arc and line must be clearly visible to pilot			CFR 23.1543	Yes  No  N/A

- All related instruments must be calibrated in compatible units	CFR 23.1543	Yes  No  N/A

Electrical System				CAR 3.694	CFR 23.1367

- Switches

- Able to carry rated current				CAR 3.682 CFR 23.1367	Yes  No  N/A

- Enough distance or insulating material between current carrying parts and the housing so that vibration will not cause shorting				CAR 3.681 CFR 23.1367	Yes  No  N/A

- Labeled as to operation and circuit controlled		CFR 23.1367	Yes  No  N/A

- Circuit Breakers/Fuses

- Circuit protection					CAR 3.690 CFR 23.1357	Yes  No  N/A

- Each resettable circuit trip free cannot be overridden 		CFR 23.1357 	Yes  No  N/A

- Fuses readily available and spare			CAR 3.692 CFR 23.1357	Yes  No  N/A

- Breakers labeled and rating 			CAR 3.691 CFR 23.1357	Yes  No  N/A

- Master Switch

- Wired to disconnect each electrical power source from the distribution systems										CAR 3.688 CFR 23.1361	Yes  No  N/A

- Switch is easily discernible and accessible to crew	CAR 3.695 CFR 23.1361	Yes  No  N/A

- Wiring inspection					CAR 3.681 CFR 23.1351 and AC43.13 chapter 11

- Chafed or frayed wires							Yes  No  N/A

- Insulation penetration							Yes  No  N/A

- Outer insulation cracking							Yes  No  N/A

- Damage or exposed wires							Yes  No  N/A

- Evidence of over heating 							Yes  No  N/A

- Evidence of arcing 							Yes  No  N/A

- Evidence of chemical contamination					Yes  No  N/A

- Wire Marking						CFR 23.1351 and AC43.13 chapter 11

- Gage, circuit, and gage size						Yes  No  N/A

- Marked 15 inched maximum intervals					Yes  No  N/A

- Grounding Points				CFR 23.1351 AC 43.13 chapter 11, AC 25-16 and AC 25-10

- Tightness of nuts (torque)							Yes  No  N/A

- Cleanliness of attach points						Yes  No  N/A

- Corrosion								Yes  No  N/A

- Sleeving and Conduits			CFR 23.1351 AC 43.13 chapter 11, AC 25-16 and AC 25-10

- Damages outer surfaces (kinks, holes, flats spots, etc.)			Yes  No  N/A

- Wear									Yes  No  N/A

- Adequate drain holes							Yes  No  N/A

- Clamping Points				CFR 23.1351 AC 43.13 chapter 11, AC 25-16 and AC 25-10

- Improper installation							Yes  No  N/A

- Clamp/wire damage							Yes  No  N/A

- Clamp cushion migration							Yes  No  N/A

- Loose wires								Yes  No  N/A

# Equipment / Furnishings

- Equipment installed functions properly 		CAR 3.622 CFR 23.1301(d)	Yes  No  N/A

- Flight manual correct for aircraft				TCDS		Yes  No  N/A

- Trim tab indicator readable and functions properly		CFR 43.13	Yes  No  N/A

- Emergency brake handle installed				CFR 21.31	Yes  No  N/A

- Batteries proper installation, & charging			 CAR 3.683 CFR 23.1353	Yes  No  N/A

- Battery vented overboard CAR 3.683 CFR 23.1353 & AC 43.13-1B PARA 11-22	Yes  No  N/A

- Battery NiCad gage for thermal run away			CFR 23.1353	Yes  No  N/A

- Thermal/Noise insulation					CFR 23.853	Yes  No  N/A

- Relief tube, corrosion areas					CFR 43.13	Yes  No  N/A

- New interior material Certs.		 CAR-3.388 and CFR 23.853/25.853	Yes  No  N/A

- Interior replaced Yes  No  New  Have Burn Certifications 			Yes  No  N/A

- Seat covers, sheep skin material Certs. 		CAR-3.388 and CFR 23.853	Yes  No  N/A

- Seat covers (automotive) require burn certification 		CFR 23.853	Yes  No  N/A

- Worn seat material CFR 25.853 for a CAR-3.388 aircraft Part 91 & 23.853, AC 43.13-1B Para 9-61												Yes  No  N/A

- Has interior been altered or material substituted 		CFR 21.303/43.11	Yes  No  N/A

- Seat back locks broke 				CAR 3.390 CFR 23.785	Yes  No  N/A

- Seat rails holes elongated Yes  No  Check AD. 		CFR 39		Yes  No  N/A

- Seating configuration, how many seats allowed 			TCDS		Yes  No  N/A

- Head rest missing and not on equipment list			CFR 91.9	Yes  No  N/A

- Seat belts for stitching, cuts, or frayed 			CFR 91.107 & 23.785	Yes  No  N/A

- Seat belts proper storage and marking 		CAR 3.715TSO-22 & 23.785	Yes  No  N/A

- Seat Belts Plastic locking ring missing, FWD  AFT  		CFR 45.14	Yes  No  N/A

- Seat belt secured when not is use				CFR 23.785(d)	Yes  No  N/A

- TSO C-22 marking on seat belts CAR 3.390/715 CFR 45.15 CFR 91.205(b)(13,14) 	Yes  No  N/A

- Shoulder harness required after July 18, 1978		CFR 23.785(g)(1)	Yes  No  N/A

- Shoulder harness required after Sept. 16, 1992 (PAX) helicopter		Yes  No  N/A

- Cabin divider(s) / Curtains / Door(s)				CFR 23.853	Yes  No  N/A

- Heating system / AD’s / decay test			CAR 3.388 CFR 23.859	Yes  No  N/A

- Cabin cooling (air conditioning), Ck /			CAR 3.393 CFR 23.831	Yes  No  N/A

- Outflow / Safety / Dump valve(s)condition		CAR 3.394 CFR 23.843	Yes  No  N/A

- Pressurization seals /boots /gaskets condition		CAR 3.396 CFR 23.831	Yes  No  N/A

- Glare shield painted flat black					CFR 23.773	Yes  No  N/A

- Door latches lock 						CFR 23.783	Yes  No  N/A

- Door sprung 					CAR 3.389 CFR 23.783	Yes  No  N/A

- Door Seals worn 					CAR 3.387 CFR 23.783	Yes  No  N/A

- Door slide track lock broken			CAR 3.387 CFR 23.783	Yes  No  N/A

##### Misc. Fuselage

- Cabin pressure controller service compressor 24 months 	CAR 3.395 CFR 23.843	Yes  No  N/A

- Pressurization seals /boots /gaskets, voids, and cracks		CFR 23.843	Yes  No  N/A

- Antenna installation doubles per 		AC43.13 2A, CFR 23.571/572	Yes  No  N/A

- Corrosion on antenna’s				CAR 3.395 CFR 23.609	Yes  No  N/A

- Fabric covered aircraft condition good  poor  	AC 43.13-1B Chapter 2	Yes  No  N/A

- Emergency exit placards 			CAR 3.768 CFR 23.1557(d)	Yes  No  N/A

- Any addition mirrors installed on wings requires Form 337	CFR 43Appen.A	Yes  No  N/A

- Condition of paint, is corrosion present NOT allowed	CAR 3.295 CFR 23.609	Yes  No  N/A

### Aircraft exterior inspection

- Wash and clean all oil, grease and dirt from aircraft	CFR 43 Appendix D	Yes  No  N/A

- Nationality and registration marks per CFR 45.29 Check 3 inch marking per date Jan. 1, 1983 and repaint. Over 30 years 2 or12 inch 					CFR 45.22(b)	Yes  No  N/A

- Rotating beacon installation proper doubler Required after 08-11-71 CFR 23.1401	Yes  No  N/A

- Anticollision light system installed 	CAR 3.705 CFR 91.209(b) / CFR 23.1401	Yes  No  N/A

- Anticollision light installed after 03/11/1996 Red or white CFR 91.206(b)(11)	Yes  No  N/A

- AFT nav light proper color white 		CAR 3.702 CFR 23.1385-1399	Yes  No  N/A

- Panel seams miss match, extra paint in front of static port	CFR 23.1325		Yes  No  N/A

- Static ports paint in hole or other things L/H  R/H  	CAR 3.665 CFR 23.1325	Yes  No  N/A

- Static vent painted over		 L/H  R/H  	CAR 3.665 CFR 23.1325	Yes  No  N/A

- Pitot heat indicator amber light					CFR 23.1326	Yes  No  N/A

- Pitot heat element operational					CFR 23.1326	Yes  No  N/A

- Pitot tube worn around hole 		Yes  No  Not plugged		Yes  No  N/A

a.  Air Speed Last inspection date _____________		CFR 23.1325	Yes  No  N/A

- Static wicks missing

- Right wing						CFR 23.867	Yes  No  N/A

- Left wing						CFR 23.867	Yes  No  N/A

- Right elevator						CFR 23.867	Yes  No  N/A

- Left elevator						CFR 23.867	Yes  No  N/A

- Rudder							CFR 23.867	Yes  No  N/A

### Landing Gear	CAR-3 and Part 23

- Correct tire and wheel for the aircraft 			CAR 3.362 CFR 23.733	Yes  No  N/A

- Tire service Main ____ R  L  Nose Tire 		CAR 3.362 CFR 23.733	Yes  No  N/A

- Tires condition wear, cuts, or weather cracking L/H  R/H   NLG  												  AC 43.13 para 9-14	Yes  No  N/A

- Landing Gear struts leaking L/H  R/H  NLG	  AC 43.13 par 9-2/4 	Yes  No  N/A

- Landing gear struts extension L/H _________ R/H __________   AC43.13 para 9-2/4Yes  No  N/A

- Landing gear fairing condition L/H ___R/H___ Nose __CFR 23.607, CFR 23.1193 	Yes  No  N/A

- Fairing cracked , Hardware missing .		 CFR 23.607/1193	Yes  No  N/A

- Landing gear fairings missing, check equipment list and W&B 	CFR 21.29	Yes  No  N/A

- Steering shimmy dampener leaking, won’t track			CFR 23.745	Yes  No  N/A

- Brake pads worn. L/H  R/H  0.100 in-thickness min. CAR 3.363 CFR23.735	Yes  No  N/A

- Brake lines condition, frayed, corrosion on fittings L/H  R/H CFR 23.735	Yes  No  N/A

- Brake rotor corrosion, warped, or under size L/H  RH 	CFR 23.735	Yes  No  N/A

- MLG strut / axle / torque links L/H condition			CFR 23.721 	Yes  No  N/A

- MLG strut / axle / torque links R/H condition			CFR 23.721 	Yes  No  N/A

- NLG strut / axle / torque links L/H condition			CFR 23.721 	Yes  No  N/A

- MLG L/H door actuating system / Hoses condition		CFR 23.1435	Yes  No  N/A

- MLG R/H door actuating system / Hoses condition		CFR 23.1435	Yes  No  N/A

- NLG door actuating system / Hoses condition			CFR 23.1435	Yes  No  N/A

- MLG L/H Landing gear actuator switch(s) condition		CFR 23.729	Yes  No  N/A

- MLG R/H Landing gear actuator switch(s) condition		CFR 23.729	Yes  No  N/A

- Repack wheel bearing					CRR 43 Appendix D	Yes  No  N/A

- Wheel nut cotter pin proper length and installed correctly		AC 43.13-1-B	Yes  No  N/A

- NLG Landing gear actuator switch(s) condition			CFR 23.729	Yes  No  N/A

- Land gear strut chrome damaged – reference manufacture maintenance manual	Yes  No  N/A

- Landing light covers cracked, missing hardware L/H  R/H 	CFR 23.729	Yes  No  N/A

- Position / Warning / Safety squat switch or (WOW) switch 	CFR 23.729	Yes  No  N/A

- Emergency extension / blow down			CAR 3.358 CFR 23.729	Yes  No  N/A

- Gear Emergency operation does it work			CAR 3.357 CFR 23.729 	Yes  No  N/A

- Landing Gear Retract/Extension System			CAR 3.356 CFR 23.729 	Yes  No  N/A

- Main landing gear locking mechanism for operation	CRR 43 Appendix D	Yes  No  N/A

- Main gear trunon strut bushings for wear	 L/H  R/H 	CFR 43.13	Yes  No  N/A

- Main gear bungee cord condition L/H  R/H  Manufacture manual		Yes  No  N/A

- Main landing & nose gear lubrication while on jacks L/H  R/H  CFR 43.13	Yes  No  N/A

- Lube type of grease used per manufacture ________________	CFR 43.16	Yes  No  N/A

- Floats and skis for security and defects			CRR 43 Appendix D 	Yes  No  N/A

Landing Gear		Specification				Actual

## Actuator cushion			Up _______	Down _______		Up _____Down____

Down lock over center		N __	L ___	R ___			N ___ L ___ R ___

Down Lock clearance		N __	L ___	R ___			N ___ L ___ R ___

Up lock clearance		N __	L ___	R ___			N ___ L ___ R ___

Up lock cable tension		N __	L ___	R ___			N ___ L ___ R ___

### Hydraulic System

- Hydraulic Distribution / Hoses condition/life limit 	CAR 3.726 CFR 23.1435	Yes  No  N/A

- Hydraulic pressure relief valve					CFR 23.1435	Yes  No  N/A

- Hydraulic accumulator charge				CAR 3.728 CFR 23.1435	Yes  No  N/A

- Hydraulic reservoir / venting					CFR 23.1435	Yes  No  N/A

- Hydraulic filter change life limit				CFR 23.1435	Yes  No  N/A

- Hydraulic electric motor brushes and condition			CFR 23.1351	Yes  No  N/A

### Flight Control/Wing

- Wing attach fittings for cracks, elongated bolt holes L/H CAR 3.317 CFR 23.572	Yes  No  N/A

- Wing attach fittings for cracks, elongated bolt holes R/H CAR 3.317 CFR 23.572 	Yes  No  N/A

- Wing L/H dents, cracks, Loose rivets, Corrosion, nav light RED 	CFR 23.603/1385Yes  No  N/A

- L/H wing Fuel vent direction check AD’s FWD  AFT 	CFR 23.975	Yes  No  N/A

- Wing R/H dents, cracks, Loose rivets, Corrosion, nav light GREEN 	CAR 3.295 CFR 23.603/1385 												Yes  No  N/A

- R/H Fuel vent direction  			FWD  AFT  CFR 23.975	Yes  No  N/A

- Flaps L/H cracks ______, loose hardware _______, Properly installed _________.	 Stop drill cracks 								CAR 3.339 CFR 23.655/697	Yes  No  N/A

- Flaps R/H cracks ______, loose hardware _______, Properly installed _________.	Stop drill cracks 								CAR 3.339 CFR 23.655/697	Yes  No  N/A

- Aileron R/H cracks ___, Loose hardware ___, Properly installed 			Yes  No  N/A

- Cable rigging loose Annual/100 hour inspection CAR 3.337 CFR 23.655/685/689	Yes  No  N/A

- Aileron L/H cracks ___, Loose hardware ____, Properly installed CAR 3.294	Yes  No  N/A

- Cable rigging loose Annual/100 hour inspection	CAR 3.337 CFR 23.655/685/689	Yes  No  N/A

- Deicer boots condition worn, holes, debonded, type CAR .7127 CFR 23.1416/1419	Yes  No  N/A

- Rudder moves up & down, bearing loose, cracks, repairs CAR 3.332 CFR 23.685	Yes  No  N/A

- Rudder / trim tab attach fittings condition, loose		CAR 3.337 CFR 23.685 	Yes  No  N/A

- Lubrication, systems lube per manufactures recommendations	CFR 43.13	Yes  No  N/A

- Electrical bonding straps broken or frayed		CAR 3.337-1 CFR 23.867	Yes  No  N/A

- Horizontal Stab L/H cracks , Loose rivets , Hardware installation and safetied , Stop drill cracks CFR 23.572 Stops  					CFR 23.675	Yes  No  N/A

- Horizontal Stab R/H cracks  Loose rivets  Hardware installation and safetied  Stop drill cracks CFR 23.572, Stops ___ 						CFR 23.675	Yes  No  N/A

- Stopped drilled holes in elevator without doublers R/H 		CFR 23.572 	Yes  No  N/A

- Stopped drilled holes in elevator without doublers L/H 		CFR 23.572 	Yes  No  N/A

- Elevator trim control system rigging			CAR 3.337 CFR 23.659 	Yes  No  N/A

- Elevator trim indicator control works			CAR 3.337 CFR 23.677(a)Yes  No  N/A

- Elevator / trim tab attach fittings L/H			CAR 3.337 CFR 23.572 	Yes  No  N/A

- Elevator / trim tab attach fittings R/H			CAR 3.337 CFR 23.572 	Yes  No  N/A

- Elevator trim / servo tab structure	 L/H		CAR 3.337 CFR 23.572 	Yes  No  N/A

- Elevator trim / servo tab structure	 R/H		CAR 3.337 CFR 23.572 	Yes  No  N/A

- Control surface attach fittings condition			CAR 3.328 CFR 23.572 	Yes  No  N/A

- Control surface balancing all primary controls after repair or paint	CAR 3.159 CFR 23.659 													Yes  No  N/A

- STOL devices / control system condition 			CFR 23.572 	Yes  No  N/A

- Boundary layer control / vortex generators, cracks and condition	CFR 23.572 	Yes  No  N/A

- Flight Control Surface Travels / Cable Tension		CAR 3.345 CFR 23.143 	Yes  No  N/A

- Gust lock, condition, worn holes			CAR 3.341 CFR 23.572 	Yes  No  N/A

- Autopilot trim indicator annual/100 hour check rigging	CAR 3.343 CFR 23.143 	Yes  No  N/A

- Autopilot system condition					CFR 23.143 	Yes  No  N/A

- Yaw damper condition				CAR 3.347 CFR 23.143 	Yes  No  N/A

- Electric trim rigging and condition			CAR 3.343 CFR 23.143 	Yes  No  N/A

- Flight control pulleys worn, broken, or frozen up		CAR 3.345 CFR 23.689 	Yes  No  N/A

- Flight control cables broken strands/rust	 Reference 	AC43.13CFR 23.689 	Yes  No  N/A

- Flight control Surface Travel/Cable Tension	CAR 3.345 CFR 23.391 to 23.459 	Yes  No  N/A

###### Travel Spec Actual	Tension Spec		Actual

Control Column		________________	___________		______

## Aileron			________________	___________		______

Aileron Trim Tab(s)	________________	___________		______

Rudder			________________	___________		______

Rudder Trim Tab		________________	___________		______

Elevator/Stabilator	________________	___________		______

Elev / Stab Tab(s)	________________	___________		______

Flap			________________	___________		______

Moveable Stabilizer	________________	___________		______

Rudder Pedals		________________	___________		______

### Engine Inspection

Engine Type Certificate Number T/C _____________________ Rev. _____________

Engine Part Number __________________________________ S/N _________________________________

Reference CAR Subpart E, CFR 23 Subpart E Powerplant, and 43 Appendix D

- Thoroughly clean the engine					CFR 43 App. D	Yes  No  N/A

- Perform engine static run					CFR 33.26/43.15	Yes  No  N/A

- Perform engine idle run R.P.M. check 				CFR 33.26/43.15	Yes  No  N/A

- Perform magneto drop check					CFR 33.37	Yes  No  N/A

- Mag “P” lead wires not cracked or broken			CFR 33.28	Yes  No  N/A

- Shut down engine and check for engine oil and fuel leaks		CFR 33.25	Yes  No  N/A

- Engine Data plate installed				CAR 3.670 CFR 45.13	Yes  No  N/A

- L/H engine Make Model/Series matches TCDS 			CFR 45.13	Yes  No  N/A

- R/H engine Make Model/Series matches TCDS			CFR 45.13	Yes  No  N/A

- Certification basic of components installed 337’s			CFR 45.15	Yes  No  N/A

- Instruments CFR 23.1305 instruments 						Yes  No  N/A

  - Cylinder head temperature	 limitations placard		CFR 43.15	Yes  No  N/A

  - Oil temperature check limitations placard			CFR 43.15	Yes  No  N/A

  - Engine 							CFR 23.1301	Yes  No  N/A

  - Accessories 						CFR 23.1301 	Yes  No  N/A

- Engine cowl loose/missing hardware Location _____ 	CAR 3.625 CFR 23.1193	Yes  No  N/A

- Firewall bent, cracked, or missing fasteners 		CAR 3.623 CFR 23.1191	Yes  No  N/A

- Firewall wire and hose grommets condition	CAR 3.623 CFR 23.1191(c)	Yes  No  N/A

- Firewall has corrosion 			CAR 3.624 CFR 23.1191(e)	Yes  No  N/A

- Engine mount structure for cracks, dents, etc. 			CFR 23.23	Yes  No  N/A

- Retorque cylinder base nuts and case half per manufacture recommendations	Yes  No  N/A

- Engine shock mount cracks, worn, hardware condition 		CFR 33.33	Yes  No  N/A

- Flex tubing condition weather cracking, worn, etc. 	CAR 3.638 CFR 23.1183	Yes  No  N/A

- Engine oil leaking Location ______________________	CAR 3.638 CFR 23.1183	Yes  No  N/A

- STC for Bracket air filter if installed & Form 337			CFR 21.111/1091Yes  No  N/A

- Air Filter dirty/foreign particles			CAR 3.605 CFR 23.1107	Yes  No  N/A

- Condition of baffle seals and installation Good  Poor  Substituted type of baffle material     						CAR 3.625 CFR 33.15/17/21& CFR 23.1043	Yes  No  N/A

- Wire chafing, fuel lines, no wires clamped under them 	CAR 3.681 AC 43.13-1B 	Yes  No  N/A

- Electrical wire Slack between supports Max 1/2 inch 	AC 43.13-1B fig.11.9	Yes  No  N/A

- Engine/Electric fuel pump condition wires, mounting Good/worn 	CFR 23		Yes  No  N/A

- Ignition harness condition Good ____ Worn ____		CFR 23		Yes  No  N/A

- Clean and gap spark plugs per engine manufactures recommendations 		Yes  No  N/A

- Rotate spark plugs per manufacture recommendation (One gasket required)		Yes  No  N/A

- Starter ring broken teeth 					CFR 23		Yes  No  N/A

- Alternator/generator drive belts condition worn, cracked, broke 	CFR 23		Yes  No  N/A

- Cylinders cracked fins, rocker cover leaking 	1__ 2__ 3 __ 4__ 5__ 6__		Yes  No  N/A

- Cylinders barrel cracked (Chrome)		1__ 2__ 3 __ 4__ 5__ 6__		Yes  No  N/A

- Cylinders check records for times & certifications1__ 2__ 3 __ 4__ 5__ 6__		Yes  No  N/A

- Exhaust stacks cracks, defects, installation	1__ 2 __ 3__ 4__ 5__ 6__ 									CAR 3.615 CFR 23. 1121 and CFR 33.21	Yes  No  N/A

- Muffler cracked, location _______, Recurring AD’s	CAR 3.617 CFR 23.1121	Yes  No  N/A

- Muffler leak test to 2 psi internal pressure 		AC 43.13-1b Para 8-49 (d)	Yes  No  N/A

- Rocker cover or push rods leaking oil past seals					Yes  No  N/A

- Valve inspection (freedom of valve rockers when valves are closed) 											manufacture recommendations	Yes  No  N/A

- Preheater shroud condition cracks, vibration		CAR 3.617 CFR 23.1101	Yes  No  N/A

- Carburetor heat box condition of holes 			CAR 3.617 CFR 23.	Yes  No  N/A

a. Proper hardware screws and nuts				CFR 23.		Yes  No  N/A

- Engine controls properly safetying  travel  AC 43.13-1B para 7-122 thru 127	Yes  No  N/A

- Engine case nuts torqued and right side up 	CFR 43 Appendix D (d)(2) 	Yes  No  N/A

- Crankcase for cracks, leaks and security of seam bolts 		CFR 33.		Yes  No  N/A

- Engine mounts for corrosion, cracks NONE Allowed		CFR 23.363	Yes  No  N/A

- Cowl flap control and operational limitations		CAR 3.625 CFR 23.1047	Yes  No  N/A

- Cowl flap check for cracks 					CFR 43.13	Yes  No  N/A

- Alternate/ Ram air / Carb heat				CAR 3.606 CFR 23.1093	Yes  No  N/A

- Turbo Waste gate (Non automatic) 				CFR 23.1091	Yes  No  N/A

- Vacuum pump lines, clamps condition   Good  Worn 	CFR 23		Yes  No  N/A

- Supercharger overall condition 	Good  Bad 		CFR 23.1109	Yes  No  N/A

- Electrical wiring cracked, burned, broken 	CAR 3.693 CRR 23.1163(b)	Yes  No  N/A

- Oil filter opening placard 			CAR 3.767 CFR 23.1557(c )(2)	Yes  No  N/A

- Drain oil						CFR 43 Appendix D	Yes  No  N/A

- Clean oil screen					CFR 43 Appendix D	Yes  No  N/A

- Replace oil filter					CFR 43 Appendix D	Yes  No  N/A

- Check filter for metal particles in accordance with manufacture   CFR 43.15, 23.1019Yes  No  N/A

- Check for metal particles or foreign matter on screens and sump drain plugs 												CFR 43 Appendix D	Yes  No  N/A

- Oil drain plug/valve condition and positive locking 	CAR 3.574 CFR 23.1021	Yes  No  N/A

- Oil radiator supporting structure for security		CAR 3.572 CFR 23.1023	Yes  No  N/A

- Oil tanks condition and free of vibration 		CAR 3.563 CFR 23.1013	Yes  No  N/A

- Hose inspection/replacement manufacture limits	 		CFR 43.10	Yes  No  N/A

- Mechanic has a master orifice for differential compression tester (MFG requirement) Yes  No  N/A

- Differential Compression Test, 80psi /60 psi cylinder 										CFR 43 Appendix D and AC 43.13-1B paragraph 8-14	Yes  No  N/A

- 1 ____ 2____ 3 ____ 4___ 5___ 6___ If 25% difference check cylinder for problems.

- Turbocharger inspect all air ducting and connections Per Manufacture Manual	Yes  No  N/A

- Exhaust pressure check system condition and leaks 5 p.s.i.		CFR 43.16	Yes  No  N/A

- Engine Condition perform completed run-up

##### Fuel System 	CAR-3 Subpart E and Part 23

- Remove cowling and clean engine of all oil and dirt	CRR 43 Appendix D	Yes  No  N/A

- Injection fuel lines Recurring AD if required every 100 hours	CFR 39		Yes  No  N/A

- Fuel bowl leaking 					CAR 3.431 CFR 23.999	Yes  No  N/A

- Fuel quantity sensor / transmitter condition			CFR 23.955	Yes  No  N/A

- Fuel boost / Aux. pump(s) bypass condition		CAR 3.449 CFR 23.955	Yes  No  N/A

- Fuel lines vibration/clamped	CAR 3.550 CFR 23.993 & AC 43.13-1B para 8-31	Yes  No  N/A

- Carburetor security, throttle arm/bushing loose 		CAR 3.551 CFR 23.994	Yes  No  N/A

- Mixture control linkage condition			CAR 3.630 CFR 23.1147	Yes  No  N/A

- Throttle control binding condition			CAR 3.628 CFR 23.1143	Yes  No  N/A

- Engine primer leaking					CAR 3.442 CFR 23.1141	Yes  No  N/A

- Remove and clean carburetor screen		 Manufacture Maintenance Manual Yes  No  N/A

- Induction System Screens condition			CAR 3.448 CFR 23.1107	Yes  No  N/A

- Fuel pump condition and AD requirement			CFR 23.991	Yes  No  N/A

- Fuel system lines and fittings conditions			CAR 3.550 CFR 23.993	Yes  No  N/A

- Fuel system drains, lock shut and drains properly			CFR 23.999	Yes  No  N/A

- Clean and inspect fuel tank strainer condition			CFR 23.977	Yes  No  N/A

- Filler cap must have electrical bonding (chain on cap)		CFR 23.973	Yes  No  N/A

- Fuel placards L/H wing Yes  No  R/H wing CAR 3.761 CFR 23.1557(c)	Yes  No  N/A

- Fuel tank caps seal condition, tight seal, flat, cracked CAR 3.445 CFR 23.973(c)	Yes  No  N/A

- Fuel tank sump drained of water			CAR 3.444 CFR 23.971	Yes  No  N/A

- Fuel tank condition for cracks, vibration, leaks			CFR 23.963	Yes  No  N/A

- Fuel line and hose condition left/right side			CFR 23.993	Yes  No  N/A

- Fuel drain valve positive locking			CAR 3.551 CFR 23.999	Yes  No  N/A

- Fuel strainer or filter condition				CAR 3.448 CFR 23.997	Yes  No  N/A

- Blistering of sealant in a fuel cell caused by corrosion		CFR 23.963(c)	Yes  No  N/A

- Fuel nonmetallic liners leaks			CAR 3.442-1 CFR 23.965((d)	Yes  No  N/A

- Unusable fuel supply check reference (TCDS)		CAR 3.440 CFR 23.959	Yes  No  N/A

- Fuel gauge reads zero when fuel tank is empty	CAR 3.440 CFR 23.1337(b)	Yes  No  N/A

- Lubricate all control rod ends and fuel system components MFG instructions	Yes  No  N/A

# Propeller Inspection

Propeller Type Certificate Number T/C _____________________ Rev. _____________

Propeller Part Number __________________________________ S/N _________________________________

- Propeller Part number and serial number 			CFR 45.11	Yes  No  N/A

- Is there a propeller maintenance record (log book)		CFR 43.2(a)	Yes  No  N/A

- If no propeller log book sign 100-hour off in airframe record	CFR 43.11	Yes  No  N/A

- Propeller seal leaking  					CFR23.907	Yes  No  N/A

- Propeller for nicks, cracks, and damage 			AC 43.13-2B Para 8-73 	Yes  No  N/A

- File marks after dressing propeller NOT allowed 		CFR 43.13	Yes  No  N/A

- Mechanic record entry after dressing nicks			CFR 43.9	Yes  No  N/A

- Propeller spinner had doubler added to repair cracks Not ALLOWED CFR 23.907	Yes  No  N/A

- Propeller spinner(s) cracks ___, NO cracks allowed nuts safety wired __ Missing screws from spinner None allowed ____ Reference Service Letters if cracked:

- Sensenich See aircraft maintenance manuals				Yes  No  N/A

- McCauley 1992-14C -part must be replaced				Yes  No  N/A

- Hartzell HC-SL-61-91 Requires a Field Approval				Yes  No  N/A

- Propeller grinding when rotating 		AC 43.13-1B para 8-2(c )(2)	Yes  No  N/A

- Corrosion pitting on blades or hub None Allowed 		CFR A35.3	Yes  No  N/A

- Paint on propeller blades, type per manufacture manual	CAR 3.295 CFR 23.609	Yes  No  N/A

- If repainted after rework type of paint applied lacquer base or polyurethane enamel and was it recorded in the propeller maintenance record					CFR 43.5	Yes  No  N/A

- STC for different propeller than original	per TCDS		CFR 21.111	Yes  No  N/A

- STC propeller check engine gages for new limitations 		CFR A35.4	Yes  No  N/A

- Is the propeller the right diameter / width		CAR 3.416 CFR 23.45	Yes  No  N/A

- Propeller ground clearance				CAR 3.422 CFR 23.925	Yes  No  N/A

- Has the propeller tips been altered (rounded or square)		CFR 43Append A 	Yes  No  N/A

- Are their repairs in the propeller maintenance records		CFR 43.9 	Yes  No  N/A

- Has the shot peen been removed after reworked at hub		CFR 43.9	Yes  No  N/A

- Has the hub seal been replaced (service life)			CFR 43.9	Yes  No  N/A

- Prop Hub is oil/grease filled and/or leaking			CFR 35.3	Yes  No  N/A

- When was the last hub overhaul				CFR 35.3	Yes  No  N/A

- Pitting corrosion on Hub NONE ALLOWED			CFR 35.3	Yes  No  N/A

- Hub, blade clamps, and pitch change mechanisms should be inspected for corrosion NONE ALLOWED									CFR A35.3	Yes  No  N/A

- Were new propeller bolts installed				CFR A35.3	Yes  No  N/A

- Were new nuts used on the propeller bolts			CFR A35.3	Yes  No  N/A

- New cotter pins installed in retaining nuts per Manufacture 	CFR A35.4	Yes  No  N/A

- Is the spinner shimmed to the spinner bracket if required 		CFR A35.3	Yes  No  N/A

- Pitch change counterweights on blade clamps should be inspected for security, safety												CFR A35.3	Yes  No  N/A

- Adequate counterweight clearance within the spinner		CFR 23.925	Yes  No  N/A

- Are the propeller blades in track				CFR 23.925	Yes  No  N/A

- De-icer boots for signs of deterioration and security		CFR 23.929	Yes  No  N/A

- Propeller total time is recorded in propeller record 		CFR 91.417(2)	Yes  No  N/A

- Propeller vibration rate				CAR 3.431 CFR 23.907	Yes  No  N/A

- Propeller clearance to ground and gear			CAR 3.417 CFR 23.925	Yes  No  N/A

- Check blade play and blade track.				CFR 43.13	Yes  No  N/A

- Lubricate the propeller assembly.  Refer to Hartzell Service Letter HC-SL-61-184 for procedure.  (If you have a Hartzell)						CFR 43.13	Yes  No  N/A

- Propeller backing plate made of composite check propeller hub for pitting corrosion	Yes  No  N/A

### Avionics Installed

Type of Avionics:  List by part number and serial number.  CAR 3.721

ALTIMETERS									Yes  No  N/A

ENCODING									Yes  No  N/A

Mfg: ACK Model: ACK 30							Yes  No  N/A

Type of Avionics: AUDIO PANEL							Yes  No  N/A

Mfg: KING Model: KMA 20							Yes  No  N/A

Type of Avionics: COLLISION AVOIDANCE SYSTEMS				Yes  No  N/A

Mfg: RYAN INTERNATIONAL CORPORATION Model: ATS 7000			Yes  No  N/A

Type of Avionics: GPS								Yes  No  N/A

Mfg: KING Model: KLN 90							Yes  No  N/A

Type of Avionics: RNAV								Yes  No  N/A

Mfg: KING Model: KNS 80							Yes  No  N/A

Type of Avionics: LOC								Yes  No  N/A

Mfg: KING Model: KI 208							Yes  No  N/A

Type of Avionics: NAV-COMM							Yes  No  N/A

Mfg: KING Model: KX 170 B Channels: 720					Yes  No  N/A

Type of Avionics: COMM								Yes  No  N/A

Mfg: KING Model: KY 197 Channels: 720						Yes  No  N/A

Type of Avionics: TRANSPONDERS						Yes  No  N/A

Mfg: KING Model: KT 76A							Yes  No  N/A

Type of Avionics: STORMSCOPE							Yes  No  N/A

Mfg: 3 M Model: WX 1000+							Yes  No  N/A

Type of Avionics: GS								Yes  No  N/A

Mfg: KING Model: KI 201							Yes  No  N/A

Type of Avionics: AUTOPILOTS							Yes  No  N/A

# Mfg: S-TEC Model: SYSTEM 60 PSS						Yes  No  N/A

Mfg: CENTURY Model: CENTURY II B						Yes  No  N/A

##### De-Icing Systems

- Known Ice System:						CFR 23.1416`	Yes  No  N/A

- Ice Lights work and condition					CFR 23.1416	Yes  No  N/A

- Prop De-Ice condition						CFR 23.1416	Yes  No  N/A

- De-Ice Type: 						CFR 23.1416	Yes  No  N/A

- Wing Tail Boots condition				CAR 3.712 CFR 23.1416	Yes  No  N/A

- Boots Condition: 					CAR 3.712 CFR 23.1416	Yes  No  N/A

- Windshield De-Ice condition					CFR 23.1416	Yes  No  N/A

- Windshield Wipers condition					CFR 23.1416	Yes  No  N/A

- Jet Intake De-Ice condition					CFR 23.1416	Yes  No  N/A

- Pitot Heat condition						CFR 23.1416	Yes  No  N/A

### Additional Equipment

- Dual Controls: 						CFR 23.777	Yes  No  N/A

- Type: Yoke.							CFR 23.777	Yes  No  N/A

- Stall Warning System works					CFR 23.703	Yes  No  N/A

- Stick Shaker works						CFR 23.672	Yes  No  N/A

- Rotating Beacon works				CAR 3.703 CFR 23.1401	Yes  No  N/A

- Strobe Light works						CFR 23.1401	Yes  No  N/A

- Taxi Lights works					CAR 3.655 CFR 23.1383	Yes  No  N/A

- Navigation Light works				CAR 3.661 CFR 23.1389	Yes  No  N/A

- Long Range Fuel						CFR 23.959	Yes  No  N/A

- Aux Fuel Qty works						CFR 23.955	Yes  No  N/A

- Single Point Refuel condition					CFR 23.953	Yes  No  N/A

- Lavatory condition						CFR 23.1561	Yes  No  N/A

- Galley condition						CFR 23.1561	Yes  No  N/A

- Cabinetry condition						CFR 23.1561	Yes  No  N/A

- Other Equipment condition				CAR 3.725 CFR 23.1561	Yes  No  N/A

- Intercom System works					CFR 23.1561	Yes  No  N/A

- Entertainment equipment CD player check for alteration form	CFR 43 App. A	Yes  No  N/A

- Gap seal kit installed						CFR 43 App. A	Yes  No  N/A

- Brackett Aero Filter STC installed				CFR 43 App. A	Yes  No  N/A

- Air Filter replacement date Bracket air filter check hours		CFR 43 App. A	Yes  No  N/A

### Special Inspections

Hours	Months	Years

- Airworthiness Directives AD’s			CFR 39

- Engine fuel and oil lines			Per Manufacture Manual

- Brake lines					Per Manufacture Manual

- Air filter engine				Per Manufacture Manual

- Air filter instruments				Per Manufacture Manual

- Wing structural areas				Per Manufacture Manual

- Hard and over weight landings			Per Manufacture Manual

- Lighting strike damage			Per Manufacture Manual

- Hail damage					Per Manufacture Manual

- Severe Turbulence Inspection			Per Manufacture Manual

- Corrosion damage Inspection			Per Manufacture Manual

- Radio Equipment				Per Manufacture Manual

- Emergency Locater Transmitter (ELT)		CFR 91.207

- Pitot Static					CFR 91.411

- Transponder 					CFR 91.411

- Rigging checks				CFR 43 App. D

- New Weight and balance aircraft for compensation / hire

- Magneto 200, 500 and etc. coil, contacts, etc. Inspection

- Rigging Inspection				Per Manufacture Manual

- Oxygen bottles Inspection (Hydrostat)		AC 43.13-1B Chapter 9 Section 3

- Lubrication Inspection			Per Manufacture Manual

- Hose Inspection Fuel and Hydraulic		Per Manufacture Manual

- Compass magnetic direction (calibration) 	CFR 23.1327

- Airspeed indicator inspections			CFR 23.1323

- Remove the rocker box covers and check for freedom of valve rockers (400-hour)

Misc., Items Aircraft Inspection

Below are some of the reported items found on New and Low time aircraft, which should stress the importance of performing a thorough inspection:

- Aileron control cable not over pulley;						Yes  No  N/A

- Aileron cable improperly installed in bellcrank/cable retaining pin was not installed;	Yes  No  N/A

- Bolts loose on the vertical and horizontal stabilizer fin attachments;			Yes  No  N/A

- Broken and cracked electrical terminals;						Yes  No  N/A

- Control cable turnbuckles not saftied;						Yes  No  N/A

- Flap follow-up cable chafing on brake line;					Yes  No  N/A

- Foreign items in fuel cells/tanks;						Yes  No  N/A

- Fuel lines twisted, bent, kinked, obstructing flow;					Yes  No  N/A

- Fuel lines chafing - inadequate clamping					Yes  No  N/A

- Incorrect propeller bolts installed;						Yes  No  N/A

- Jam nuts drilled but no safety wire installed;					Yes  No  N/A

- Lock clips missing from control cable turnbuckles;				Yes  No  N/A

- Loose rivets in horizontal stabilizer leading edge;					Yes  No  N/A

- Main wheel tires do not clear wheel bays;					Yes  No  N/A

- Numerous drill chuck marks in aft face of pressure bulkhead. 			Yes  No  N/A

- Oil lines leaking at connections;						Yes  No  N/A

- Primer line "T" fitting not installed;						Yes  No  N/A

- Propeller blade retention ferrules under torqued;					Yes  No  N/A

- Elevator trim cable wrapped around primary rudder control cable; 			Yes  No  N/A

- Rivet holes drilled but rivets not installed, different areas;				Yes  No  N/A

- Rudder cable bellcrank attach bolts loose;					Yes  No  N/A

- Rudder cable bolts fitted upside down; and					Yes  No  N/A

- Unreliable fuel quantity indications.						Yes  No  N/A

Sample AD Compliance List

AIRWORTHINESS DIRECTIVE COMPLIANCE RECORD

N-Number _____________________________

Make _________________________ Model __________________  S/N________________________________

| AD Number | Subject | Date and Hour of Compliance | Method of Compliance | One Time | Recurring | Next due | Authorized Signature |
| --- | --- | --- | --- | --- | --- | --- | --- |

Sample Logbook Unairworthy Maintenance Entry

Sample Logbook Airworthy Maintenance Entry

FAA Web Site Links: (http://www.faa.gov)

- Type Certificate Data Sheets (TCDS) http://www.airweb.faa.gov/Regulatory_and_Guidance_Library/rgMakeModel.nsf/MainFrame?OpenFrameSet

- Regulations, AC’s. and & Forms:  http://www.faa.gov/mechanics/regs_policy/

- Airworthiness Directives:

http://rgl.faa.gov/Regulatory_and_Guidance_Library/rgAD.nsf/MainFrame?OpenFrameSet

Life limits CFR 43.10

This checklist is not exhaustive and does not supersede Manufacture’s publications and is up-dated periodically!

Calendar/ Hourly Life limited Items:			Years. 	Hours.

# Airframe

Gyro air filters, central 					5	500

Non-Teflon fuel, oil, and hydraulic hoses			15	3000

Teflon fuel, oil, and hydraulic hoses 			20	4000

Seat belt / shoulder harness webbing 			20

Stabilizer attach bolts 					25	6000

Wing bolts 						25	6000

# Engine

Engine shock mounts 					15	TBO

Non-Teflon fuel, oil, and hydraulic hoses 			8	TBO

Teflon fuel, oil, and hydraulic hoses 			15	TBO

Continental Engines						2000 SL 98-9

Special Inspection Items: 				Years. 	Hours.

# Airframe

Gyro air pump carbon vanes 				6	500

Electric hydraulic pump motor 				15	500-1500

Electro mechanical gear actuator 				15	3000

Gear actuator motor brushes				2 	250

Gear motor internal inspection / lubrication 			15	3000

Flight control trim actuator(s) 				15	4500

Electrical flap actuators/motors 				20	4000

Stabilizer mounting bolts torque inspection 			5

Wing attach bolts torque inspection 			5

# Propeller

Fixed pitch propeller recondition 				6	2000

Mounting hardware 					20	2000

Constant speed propeller overhaul 				6	2400

Prop governor reseal 					15	1500

Governor (Woodward)					5	2400

Accumulators						5	1800

# Engine

Alternator							500

Gear drive alternator internal inspection 			5	300

Belt driven alternator internal inspection 			5	500

Internal magneto inspection 				5	500

Valve inspection/dry lash clearance 			15	TBO

Cam / cam follower inspection (TCM engines) 		15	mid life

Bendix fuel injector servo overhaul 				20	TBO

Pressure carburetor overhaul 				20	TBO

Primer nozzles cleaned and spray pattern 			5

Continental unmetered fuel pressure check 			2	400

Diaphragm fuel pumps overhaul 				20	TBO

Internal starter inspection 					5	mid-life

Turbocharger oil inlet check valve(s) 			10	1000

Turbocharger oil scavenge check valves(s) 			10	1000

Hydraulic wastegate actuator(s) resealing 			10	1000

This is only a guide and should not be considered FAA approved data for life limits.  Consult the manufacture recommendations, type certificate data sheets (TCDS), AD's, or the limitations section of FAA-approved airplane or rotorcraft flight manuals.

| Reg # ___________ | Manufacturer | Model Number | Serial Number |
| --- | --- | --- | --- |
| Aircraft |  |  |  |
| Engine #1 |  |  |  |
| Engine #2 |  |  |  |
| Engine #3 |  |  |  |
| Engine #4 |  |  |  |
| Propeller #1 |  |  |  |
| Propeller #2 |  |  |  |
| Propeller #3 |  |  |  |
| Propeller #4 |  |  |  |
| Category | Manufacturer | Part Number | Serial Number |
| Accumulators |  |  |  |
| Air Conditioner |  |  |  |
| Air Data Inertl Ref Unit |  |  |  |
| Air Filter |  |  |  |
| Airspeed Indicator |  |  |  |
| Alternators |  |  |  |
| Altimeter |  |  |  |
| Angle of Attack sensor |  |  |  |
| Attitude Hdg Reference Sy |  |  |  |
| Auto-pilot |  |  |  |
| Autopilot Servo |  |  |  |
| Auxiliary Power Unit |  |  |  |
| Ball/Swivel Quick Connctr |  |  |  |
| Batteries |  |  |  |
| Brake Assemblies |  |  |  |
| Cabin Doors |  |  |  |
| Cabin Superchargers |  |  |  |
| Carburetors |  |  |  |
| Circuit Breakers |  |  |  |
| Cockpit Voice Record |  |  |  |
| Coffee Makers |  |  |  |
| Combustion Heaters |  |  |  |
| Cylinder Assemblies |  |  |  |
| Cylinder, Propane |  |  |  |
| DME-Dist Measuring |  |  |  |
| Dusting/Spraying Ops |  |  |  |
| EFIS-Elec Flight Inst Sy |  |  |  |
| ELT |  |  |  |
| Emergency/Survival Equip. |  |  |  |
| Emergency Pwr Supplies |  |  |  |
| Engine Gage Units |  |  |  |
| Fire Detectors |  |  |  |
| Fire Ext Dischargers |  |  |  |
| Fire Extinguishers |  |  |  |
| Flight Data Recorder |  |  |  |
| Flight Director Sys |  |  |  |
| Flight Management Sy |  |  |  |
| Floats |  |  |  |
| Fuel Cells |  |  |  |
| Fuel Flow Transmitter |  |  |  |
| Fuel Injected System |  |  |  |
| Fuel Pumps |  |  |  |
| Fuel Selector Valve |  |  |  |
| Fuel System |  |  |  |
| GPWS(Gnd Prxmty Warn Sys) |  |  |  |
| Gear Boxes |  |  |  |
| Glass Fiber Fabrics |  |  |  |
| Glider Tow Couplings |  |  |  |
| Global Positioning System |  |  |  |
| Governors |  |  |  |
| Hardpoint Assemblies |  |  |  |
| Hoists |  |  |  |
| Horizontal Sit Ind-HSI |  |  |  |
| Hoses |  |  |  |
| Ignition Switches |  |  |  |
| Instrument Filters |  |  |  |
| Instrument Landing Sys |  |  |  |
| Integr. Avionics Computer |  |  |  |
| Intercom/System |  |  |  |
| LORAN |  |  |  |
| Landing Gear |  |  |  |
| Lavatory Receptacles |  |  |  |
| Lighting |  |  |  |
| Magnetic Compass Sys |  |  |  |
| Magnetos |  |  |  |
| Navigation Systems |  |  |  |
| Oil Coolers |  |  |  |
| Oil Filters |  |  |  |
| Oxygen Masks |  |  |  |
| Oxygen System |  |  |  |
| Parachutes |  |  |  |
| Piston Pin |  |  |  |
| Pistons |  |  |  |
| Pitot Static Heater |  |  |  |
| Protect Breathing Equip |  |  |  |
| Push-pull Control |  |  |  |
| Radio Magnetic Indicator |  |  |  |
| Receiver(s) |  |  |  |
| Refueling System |  |  |  |
| Safety Belts |  |  |  |
| Seat Track Fittings |  |  |  |
| Seats |  |  |  |
| Smoke Detectors |  |  |  |
| Spark Plugs |  |  |  |
| Speaker(s) |  |  |  |
| Standby Vacuum Systems |  |  |  |
| Starter |  |  |  |
| Starting Vibrator |  |  |  |
| TCAS Terr Collision Avoid |  |  |  |
| Tires |  |  |  |
| Traffic Advisory System |  |  |  |
| Transducers |  |  |  |
| Transponder |  |  |  |
| Turbine Power Conversion |  |  |  |
| Turbochargers |  |  |  |
| Turn and Bank Indicator |  |  |  |
| Unapproved Parts |  |  |  |
| Vacuum Pumps |  |  |  |

# Text boxes

September 08, 2007.Total time 853.00 hours Tach reading 420.80 I certify that this aircraft has been inspected in accordance with an annual inspection and a list of discrepancies and unairworthy in accordance with Part 43 Appendix D items dated (insert date) has been provided for the aircraft owner or leasee.

George B. Jones IA272182

September 08, 2007. Total aircraft time 853.00 hours. Tach reading 420.80 Replaced right main wheel bearing, P/N 19844, upper bushing in R&L landing gear frames, both brake hoses, P/N 34052, and bled brakes. I certify that this aircraft has been inspected in accordance with an annual inspection and was determined to be in airworthy condition in accordance with Part 43 Appendix D. or (Manufacture manual revision 123 date 12/14/2010

George B. Jones IA272182